## Slide 2: ChaProEV is a generic activity-level model
Detailed
activity-based
models
Micro-scale
agent-based
models
Usage scope
Detail level
Coordinate methods and defintions
Generic activity level
National/EU:
Explain to stakeholders
Input to energy system models
Specific activity level for neighbourhoods
Local/municipal
Advice to policy makers
Show impact at neighbourhood level
Detailed agentic behaviour at individual level
Local and global:
Identify emergent behaviours
Support cost-effective decision-making
Uses micro-level models and zoom out/aggregate to the city level
Notes: For LABS: Local means using micro level models and global means zooming out from that micro level and aggregating bck at the city level.

## Slide 3: Structure of ChaProEV

## Slide 5
Legs

## Slide 6
Trips
Commute to work
Commute to work and leisure
Leisure only
Weekend trip
Holiday outward
Holiday back
Stay put home
Stay out holiday

## Slide 7: ChaProEV delivers baseline profiles and boundary conditions for energy system models
Baseline/ unmanaged charging profiles
Boundary conditions:
Demand of departing vehicles for upcoming leg
Effective available charge/discharge power
Connectivity
Effective efficiencies
EV model within energy system/optimisation model
Managed/optimised profiles
Effective profiles

## Slide 8: Basic approach: Fleet-level averages
Charging profile
Weighted sum with average properties

## Slide 9: Stochastic approach: Repeated random draws for individual vehicles
Trip for that day
Events
Repeat
Sum
Charging profile

## Slide 10: Each approach has its own uses
Stochastic approach
Fleet approach
Simple
Reflects fleet behaviour
Is appropriate for basic charging behaviour
Sufficient for general insights and as supply for energy system models
More complex
Shows individual vehicle behavior
Allows for more complex charging behaviour (including decisions based on state of charge and more complex network interactions)
Allows for deeper policy testing

## Slide 11: Add more features with stochastic approach
Grid models
User behaviour
Charging infrastructure
Charging strategies

## Slide 12: Grid: transformer balancing/topological effects
Grid models
User behaviour
Charging infrastructure
Charging strategies
Transformer balancing
Topological effects
versus

## Slide 13: Charging: Curve effects and connection management
Grid models
User behaviour
Charging infrastructure
Charging strategies
Connection management
Charging curve effects
State of Charge (SoC)
Charging Power (kW)
0%
20%
40%
60%
80%
100%
50
100
150
Add more chargers to connection (satellite poles)

## Slide 14: Behaviour: Peer effects and balance of preferences
Grid models
User behaviour
Charging infrastructure
Charging strategies
Peer effects
Balance of preferences

## Slide 15: Strategies: How and which trigger
Grid models
User behaviour
Charging infrastructure
Charging strategies
Adaptive/ spread out
Full power until filled
Available power modulation
Charge only if battery below given threshold

## Slide 16: Create dashboard to test variants of tested elements
Grid models
User behaviour
Charging infrastructure
Charging strategies
Charging profile
Baseline
Variant

## Slide 17: ChaProEV availability
Source code
https://github.com/TNO/ChaProEV
Library
https://pypi.org/project/ChaProEV/
Add scenario files and call functions within your model or independently
Understand how the model works